## Slide 1
Prediction of Quality Degradation for Mobile Video Streaming Apps: A Case Study using YouTube Dhruv Jain*, Swapnil Agrawal*, Satadal Sengupta*, Pradipta De#, Bivas Mitra*, Sandip Chakraborty* *Indian Institute of Technology Kharagpur, India #State University of New York (SUNY), Korea | 
OBJECTIVES
  Growing popularity for developing streaming media applications over HTTP – new challenges for managing video quality over mobile devices.
  Develop a light-weight method for early detection of network capacity degradation using traffic characteristics of mobile streaming video apps.
  Prediction of possible video quality degradation and video re-buffering events by observing the traffic patterns of video apps, such as YouTube.
MOTIVATION
  Streaming video services have witnessed a shift from conventional delivery via the real time protocol (RTP) or real time streaming protocol (RTSP) to streaming over data service protocols like HTTP or HTTPs.
  Streaming over HTTP/HTTPs has advantages in terms of data transfer flexibility and network scalability
  However, detection of sudden network capacity degradation and thereby prediction of end-user’s quality of experience (QoE) becomes difficult.
  Metrics such as TCP goodput and current buffer size can be used to estimate connection quality – but they have limitations.
RESULTS
DATA COLLECTION
ANALYSIS OF YOUTUBE VIDEO DATA
  Observations:
  When network quality is favourable:
  Traffic pattern exhibits periodic bursts of almost similar periodicity and equal burst sizes.
  Bursts are short but sharp; small burst duration and large peak size indicate good quality video.
  Peak size and the burst duration have a direct relationship with the video resolution.
  When channel quality drops:
  Gradual drop in the peak size of bursts; burst duration tends to become large (bursts widen).
  During re-buffering, wider burst duration is observed, although with a high peak size.
VIDEO QUALITY PREDICTION
  Prediction of video quality switch from good to bad by setting threshold over peak size & burst duration.
  2 thresholds defined – the peak size threshold (TPS) and the burst duration threshold (TBD).
  Outline of the algorithm:
  When a data packet is received, decision is taken on whether it belongs to the same burst or a diff. burst, depending on a threshold Tburst
  For every such burst, 2 parameters are computed:
  Burst Age Ab = packet arr. time–burst start time
  Estimated Peak Size Pb = (b*TBD)/Ab
  4 zones defined based on pairs (TPS, TBD) and (Ab, Pb):
  Good Connectivity Streaming Zone (GCSZ): Ab ≤ TBD, Pb ≥ TPS – indication that bursts are short and sharp.
  Bad Connectivity Streaming Zone (BCSZ): Ab > TBD and Pb < TBD – bursts are small and wide.
  Re-buffering Zone (RZ): Ab > TBD and Pb ≥ TPS
  Confusion Zone (CZ): All other cases – no decision
Data Collection Particulars | 
Representative app | YouTube
Reason for choice | Exhibits different traffic characteristics in different network conditions
No. of volunteers | 4
Data collection period | 3 months
Smartphone make | Motorola Moto-X Gen. 2
Channels | Wi-Fi and Cellular
Video resolution | Fixed resolution 240p, 360p, 480p, 720p and also auto-mode
Ground truth | Manual timestamping of re-buffering and video resolution degradation