## Slide 1: MoViDiff Enabling Service Differentiation for Mobile Video Apps Speaker: Satadal Sengupta Indian Institute of Technology Kharagpur, India
Co-authors:
Vinay Kumar Yadav (IIT Patna) Niloy Ganguly (IIT Kharagpur)
Yash Saraf (IIT BHU) Sandip Chakraborty (IIT Kharagpur)
Harshit Gupta (IIT Kharagpur) Pradipta De (Georgia Southern Univ.)

## Slide 2: What is Service Differentiation?
Bandwidth sharing among different classes of traffic
Sharing based on context and user-requirement
Example: DiffServ Architecture
Enables Fine-Grained Bandwidth Control

## Slide 3: Why Mobile Video Apps?
Video most data-consuming service on mobile
Expected to rise to 3/4th of all mobile data traffic by 2020 (Cisco Visual Networking Index Report)
Bandwidth control on video apps most relevant
Notes: CAGR - Compound Annual Growth Rate

## Slide 4: Types of Mobile Video Apps
Streaming Video Apps
  Data-hogging apps
  Pre-recorded
  Entertainment
  Can withstand bandwidth drop
Interactive Video Apps
  Consume lesser data
  Interactions/meetings
  Sufficient bandwidth vital
  Easily overshadowed by streaming video apps
Interactive apps more bandwidth-sensitive than Streaming apps
Star India
Notes: CAGR - Compound Annual Growth Rate

## Slide 5: Service Differentiation in Mobile Video Apps – Where is it Useful?
Multiple devices, playing different types of videos, connected to single router (or tethered to a phone) – gateway device
Sharing of fixed (low) bandwidth
Some such scenarios:
  Households
  Academic/Enterprise Set-ups
  Personal mobile hubs
Goal: Acceptable quality at all connected end-devices

## Slide 6: Personal Mobile Hub – Use-case
Same user on different video apps on different devices
Tethered to the same hotspot, served by a Gateway Device
Examples: Remote tech/medical help, simulated movie dates
Can different bandwidths be allocated to the devices?

## Slide 7: The Problem Statement
In the presence of simultaneous traffic flows from a streaming video app and an interactive video app,
in the presence/absence of background non-video traffic,
allocate bandwidth at the gateway device such that experiences at both apps remain satisfactory

## Slide 8: Core Challenges
Core Research Challenge:
Question: How to classify traffic originating from different apps?
Approach: Attribute every single data packet to its origin app
Core Implementation Challenge:
Question: If the origin of traffic is known, how to achieve differentiation in terms of service?
Approach: Intercept a packet, schedule it according to desired Quality of Service (QoS)
Resolving both challenges leads to the overall solution

## Slide 9: Traffic Classification in Mobile Apps: Why not a Solved Problem?
Traffic classification relies on identifying unique signatures
Common signatures used to identify desktop applications:
  Port number used by an application
  Host address of the server
  Other protocol-specific identifiers in the network packets
Unique situation in case of mobile apps:
  Port-based identification invalidated since most traffic tunnelled over HTTP
  Inspection for protocol-specific identifiers not possible on encrypted packets
  Introduction of protocols like QUIC, which allow for end-to-end encryption
Traffic Classification in Mobile Apps a Non-Trivial Problem

## Slide 10: Traffic Classification: Related Work
Traffic identification based on deep packet inspection (DPI)
  HTTP user-agent field (Xu et. al. – IMC 2011)
  In-app advertisements (Tongaonkar et. al. – PAM 2013)
  Signature strings in packet content (Yao et. al. – MobiCom 2015)
  Limitation: Ill-suited for encrypted traffic – involves peering inside the packet
Identification of flow patterns in video applications
  Patterns in Skype traffic (Yuan et. al. – ICNC 2014, Jesudasan et. al. – CAIA 2010)
  Youtube on PC (Ameigeiras et. al. – Tranx. on Emerging Telecommunications Technologies 2012, Ramos-Munos – IEEE Wireless Communications 2014)
  Limitation: Proposed for web versions – we build on these studies
Need for a classification technique for encrypted mobile app traffic

## Slide 11: Experimental In-Laboratory Setup
Testbed Setup
Trace Collection Scenarios
Pre-processing: Flow Segregation (based on 5-tuples)

## Slide 12: Traffic Classification: Observations
Traffic distribution for different kinds of apps
Distinct patterns for different kinds of apps

## Slide 13: Traffic Classification: Packet-level Features
Interesting packet-level features – from observations
Packet-size (PS)
Inter-arrival Time (IAT)
Bandwidth (BW)
Why are these features useful for classification?

## Slide 14: Packet-size Distribution
YouTube Skype
Packet-size saturates at maximum transmission unit (MTU) for YouTube, distributed over lower values for Skype

## Slide 15: Packet-size Distribution: In Summary
Streaming Video Apps – Packet-size saturates at a fixed value, which is the max. transmission unit (MTU) for transport layer, for Wi-Fi
Streaming Video Apps – Packet-size distribution shows (almost) no variation with video resolution
Interactive Video Apps – Significant variation over a range, sometimes with bandwidth
Packet-size distribution consistent for individual apps, but marked difference between streaming and interactive traffic
Packet-size can be a classification feature

## Slide 16: Inter Arrival Time (IAT) Distribution
YouTube
Skype
Sharp change in IAT at particular values for YouTube, gradual change for Skype

## Slide 17: IAT Distribution: In Summary
Sharp changes in IAT value for streaming traffic, gradual change for interactive traffic
Behaviour can be traced back to bursty pattern of streaming traffic
IAT values generally low for interactive traffic; however, chance of confusion with inter-burst IATs of streaming traffic
Inter-Packet Timing Average (IPTA) – moving average, serves as a better classification parameter
Variation of values with bandwidth – bandwidth is a potential feature
IPTA and Bandwidth can be classification features

## Slide 18: System Architecture
Implementation – in-depth
Identify app launch from handshake packet
Machine learning based traffic classifier
Features – subset of (packet-size, IPTA, bandwidth)
Implemented pymovidiff
Based on NFQueue lib.
Priority parameter λ

## Slide 19: System Architecture: App Identifier
Inspect handshake packets exchanged when a new network-based app is launched
SSL server certificate unique for an app
One-time low-overhead process to identify launch of an app
Detecting app launch does not ensure that each packet is uniquely identified
How to Ensure Packet-level Identification?

## Slide 20: System Architecture: Flow Differentiator
Data-Control Classifier
Control Packets – ARP, DNS, IGMP, ICMP, NTP, DB-LSP-DISC (Dropbox Lan Sync Protocol), etc.
Control packets do not carry video content – removal ensures better classification accuracy
SVM with packet-size as the lone feature – control packets are typically much smaller than data packets
Avg. accuracy of 99% achieved
Weeding out Control Packets

## Slide 21: System Architecture: Flow Differentiator
Flow Classifier
Takes a single data packet as input, and classifies it into belonging to one of the target apps (streaming/interactive), or background traffic
Classification based on a subset of the following features:
  Packet-size, IPTA, Bandwidth
Binary SVM (absence of background traffic) Multi-class SVM (presence of background traffic)
Packet-level Classification

## Slide 22: System Architecture: Service Differentiator
Implemented Python module called pymovidiff
Based on the NetFilterQueue (NFQueue) module for packet interception and scheduling
Pymovidiff works with a producer thread and a consumer thread, scheduling packets based on user priority parameter λ
Packet Scheduling ensuring Service Differentiation

## Slide 23: Evaluation
MoViDiff as a Service Differentiator
  Bandwidth allocation
  Impact on video quality
MoViDiff as a Traffic Classifier
  Absence of background traffic
  Presence of background traffic

## Slide 24: Evaluation
MoViDiff performance as a Service Differentiator
The bandwidth allocation of preferred application Skype increases while for YouTube it decreases
Despite bandwidth allocation, the YouTube stream is acceptable as shown by the PSNR (Peak-Signal-to-Noise-Ratio) – Result of adaptive HTTP
MoViDiff works successfully as a Service Differentiator

## Slide 25: Evaluation
MoViDiff performance in Absence of Background Traffic
Packet-Size as the Only Feature
Good Classification due to distinct Packet-sizes

## Slide 26: Evaluation
MoViDiff performance in Presence of Background Traffic
Packet-Size as the Only Feature
Good Accuracy for YouTube & HotStar Poor Classification for TED – Similar PS

## Slide 27: Evaluation
MoViDiff performance in Presence of Background Traffic
One Feature vs. Multiple Features for TED
Average Precision Average Recall Average Accuracy
Classification Performance improves for TED

## Slide 28: Conclusion
Service differentiation system for Mobile Video Apps
Based on a Traffic Classification core
Traffic Classification based on Packet-level features
Performance improves on adding additional features for poorly-performing cases

## Slide 29: Work in Progress: Can we do Better?
Why? Near 100% accuracy desired for classification in real-time.
Identify additional features for better classification
Bit-pattern similarity among encrypted packet payloads
Hypothesis: Payloads encrypted with same algorithm and key should have high similarity, especially towards the beginning
Similarity Measures: e.g., K-L Divergence on FFT of bit-streams

## Slide 30: Thank You! Questions?

## Slide 31: Backup

## Slide 32: Is the Use-Case Practical?
Prevalent in many scenarios:
  Remote medical help – Remote tech support
  Long-distance couple watching a movie together
Applications which combine chatting and streaming experience
  Rabbit (https://www.rabb.it/)
Practical, and increasingly prevalent!

## Slide 33: Packet-size Distribution: Streaming Video Apps
Packet-size saturates at maximum transmission unit (MTU)

## Slide 34: Packet-size Distribution: Interactive Video Apps
  Skype Google Hangouts
ooVoo
Packet-size varies a lot, sometimes with bandwidth

## Slide 35: IAT Distribution: Streaming Video Apps
Sharp change in IAT at a particular value

## Slide 36: IAT Distribution: Interactive Video Apps
Gradual change in IAT

## Slide 37: Evaluation
MoViDiff performance as a Traffic Classifier
SVM module (scikit-learn, C=1, RBF kernel) – 70/30% training-testing
Performance of Data-Control Classifier
Near-Perfect Data-Control Classification

## Slide 38: Evaluation
MoViDiff performance for a Video App vs. Mixed Traffic from Background Apps
Packet-Size as the Only Feature
Good for Interactive, Poor for Streaming (except YouTube)

## Slide 39: Evaluation
MoViDiff performance in Presence of Background Traffic
Packet-Size, IPTA, and Bandwidth as Features
Classification Performance improves for TED